## Slide 1
Drysuit Course

## Slide 2: Course Aim and Programme
To teach members the correct and safe techniques for drysuit diving
  Theory lesson 1: Drysuits and Equipment
  Theory lesson 2: Drysuit Diving Techniques
  Practical lesson: Sheltered Water
    Using a drysuit
  Practical lesson: Open Water
    Drysuit dive experience

## Slide 3
Drysuit Course
Drysuits and Equipment

## Slide 4: Section 1: Drysuits and Equipment
  Introduction: lesson objectives
  Review of physics: effects on a drysuit diver
  Types of drysuits
  Undergarments
  Suit controls
  Use of Buoyancy Compensator with drysuit, for:
    Emergency buoyancy
    Escape from depth
    Escape from inversion
    Emergency breathing
  Selection, care and maintenance
  Summary

## Slide 5: Why use a drysuit in the UK
Heat Loss In Water
  25 x faster than air
400 C
300 C
200 C
100 C
00 C
Normal body
temperature
No suit
required
Wetsuit / Drysuit
required
Drysuit
required
370 C
  Cold water increases rate of heat loss
  Insulation consideration for divers in UK
  Drysuits used extensively in the UK

## Slide 6: Introduction: Lesson objectives
At the end of this lesson students will be able to:
  Identify the different types of drysuit
  Identify the features they embody
  Explain why a BC should be used with a drysuit
  Identify the potential problems and their solutions
  Show an understanding of theory knowledge through an end of lesson test

## Slide 7: Review of Physics
Session Objectives
  Review pressure / volume changes
  Behaviour under pressure and underwater
  Explain ‘squeeze’ and how to avoid it
  Loss of buoyancy and how to regain it
  Explain ‘air migration’ in a suit and how to control it

## Slide 8: Air and Water Pressure
0m
10m
30m
20m
1/2
1/3
1/4
AIR
1
Depth
0m
10m
30m
20m
1/2
1/3
1/4
Air + Water
Pressure
2 bar
Air
Pressure
1 bar
Air + Water
Pressure
3 bar
Air + Water
Pressure
4 bar

## Slide 9: Behaviour under pressure
Descending on dive
  Drysuit surrounds body with air providing
    Insulation
    Buoyancy
  On descent water pressure causes compression
    Suit ‘squeeze’ can be caused
    Loss of buoyancy
  Compensate by injecting air into drysuit
    Reduces ‘squeeze’
    Regains buoyancy

## Slide 10: Behaviour underwater
Lung volume
Comfort air in suit
Boyles Law
For a fixed mass of gas at constant temperature, the pressure is inversely proportional to the volume
Balloons / Lungs
Depth
0m
10m
30m
20m
Air + Water
Pressure
2 bar
Air + Water
Pressure
3 bar
Air + Water
Pressure
4 bar
Air
Pressure
1 bar
AIR
1 bar
AIR
2 bar
AIR
3 bar
AIR
4 bar
AIR
1
1/2
1/4
1/3

## Slide 11: Behaviour underwater
During dive
  ‘Air migration’ – movement of air bubble within drysuit
  Change of attitude must be considered
    Inversion
    Trim
    Inability to dump excess air

## Slide 12: Behaviour underwater
Ascending on dive
  On ascent air expands
    Migrates to highest point
    Increases buoyancy
    Increases chance of ‘air migration’
    Seals may ‘pop’ and release air
    Rate of ascent will increase
  Excess air must be released under control
    Use dump valve or control valve
    Regain buoyancy
    Reduce ascent speed

## Slide 13: Using SCUBA Equipment Warning
  Never hold your breath - lungs will expand on ascent = damage
  Similarly drysuit air will expand on ascent
  May cause seals to ‘pop’
  So dump excess air in a ‘controlled manner’
SCUBA delivers Breathing Gas at Ambient Pressure
2 bar
1 bar
3 bar
0m
10m
20m
AIR
1 bar
AIR
2 bar
AIR
3 bar
AIR
3 bar
AIR
2 bar

## Slide 14: Types of drysuits
Foamed / crushed neoprene drysuit
  Good insulation
  Suit buoyant
  Neoprene seals
Membrane drysuit
  Minimal insulation – need for warm undergarments
  No inherent buoyancy
  Latex seals

## Slide 15: Types of drysuits: principles
Membrane Dry Suit
Body
Water
Under Suit
Air
Neoprene Dry Suit
Body
Air
Water

## Slide 16: Types of drysuits
Zip entry
  Shoulder
  Front entry
Seals
  Neck and wrists
  Neoprene
  Latex – tapered, trim to size
Hoods
  Separate
  Integrated
Gloves
  Neoprene
  Dry gloves

## Slide 17: Types of drysuits
Price range
  Neoprene - £550 – £1000+
  Membrane - £250 – £1000+

## Slide 18: Undergarments
Woolly bears
  Warm, bulky, quick-drying,
  Loose-fitting
  Various materials
Base layers
  Warm, less bulky, quick-drying
  Tighter fit
  Wicks moisture to outside
Track suits
  Various styles
  Suitable for summer use

## Slide 19: Suit controls
Inflation systems:
  Push button control
  Direct from first stage
  Push / pull fitting for hose connection
Vent systems:
  Cuff dump
    positioned on arm near cuff
    vented by lifting arm
  Automatic / adjustable dump
    positioned on upper arm near shoulder
    venting set automatically
    manual over-ride
Possible interference by BC and other kit
Inflator
Auto
vent

## Slide 20: Use of BC with drysuits
Drysuit is NOT a lifejacket
BC must be worn to provide:
  Emergency face-up buoyancy on surface
  Assists in escaping inversion
  Independent source of emergency buoyancy (CBL)
  Emergency buoyancy for free ascents
  Passive, fully kitted diver likely to float face-up but
    Face submerged and awash
Drysuit also independent source of buoyancy
Neoprene suits lose buoyancy with depth
Membrane suits have no neutral buoyancy
If drysuit holed, will lose air and buoyancy.
Regained by:
  Inflating BC
  Dumping weightbelt

## Slide 21: Use of BC with drysuits
Escape from inversion at surface
If air migrates to feet:
  Inflate BC to level off and get vertical again
  Buddy could assist
Inversion not usually a problem if suit correct fit for wearer
If inversion does occur it implies:
  Too much air in suit
  Heavy equipment worn too high (cylinders)
Correct buoyancy important for diver stability and comfort

## Slide 22: Selection, care and maintenance
Which suit is for you?
  Big bodies need less insulation than smaller ones
Neoprene drysuits:
  Thinner / fewer undergarments
  Warmer if flooded
  Retains some buoyancy when flooded
  Could have reduced flexibility
  Colour usually black!
Membrane drysuits
  Thicker / more undergarments required
  No insulation if flooded
  No buoyancy when flooded
  More flexible movement
  Wide selection of colours

## Slide 23: Selection, care and maintenance
Care and maintenance
  Rinse in fresh water
  Allow to dry naturally
  Avoid direct sunlight / excessive heat
  Check and clean zip
  Lubricate with beeswax
  Talc all seals before storing
Store by:
  Hanging from neck on suitable hanger
  Hanging by boots on designed hanger
  Loosely roll

## Slide 24: Summary
  Review of physics
  Types of drysuits
  Undergarments
  Suit controls
  Use of Buoyancy Compensator with drysuit, for:
    Emergency buoyancy
    Escape from depth
    Escape from inversion
    Emergency breathing
  Selection, care and maintenance

## Slide 25: End of lesson test
  What are the two types of drysuit?
  What is ‘suit squeeze’?
  What are the characteristics of a neoprene suit?
  What are the characteristics of a membrane suit?
  Name two types of undergarment that can be worn
  Name the two controls found on a drysuit
  Is a drysuit suitable as a lifejacket?
  Can a drysuit be used as a source of buoyancy in an emergency?
  What is ‘air migration’?
  What maintenance should be used on a drysuit?

## Slide 26
Drysuit Course
Drysuit Diving Techniques

## Slide 27: Section 2: Drysuit Diving Techniques
  Introduction: lesson objectives
  Drysuit preparation and dressing
  Correct weighting and buoyancy checks
  Drysuit diving in safety
  Emergency actions
    ‘Blow-up’
    Inversion
    Flooding
  Drysuit diver rescue
  Summary

## Slide 28: Introduction: Lesson objectives
At the end of this lesson students will be able to:
  Correctly prepare and dress in a drysuit
  Explain how to dive safely in a drysuit
  Explain actions to be taken in the case of an emergency
  Explain the action to take in rescuing a drysuit diver

## Slide 29: Preparation and dressing
Check suit as it is unpacked:
  Check seals not perished
  Check for potential damage
  Talc / lubricate seals
  Lubricate zip
Dress in drysuit undergarments
Put on suit
  Invert top for easy access
  Feet first
  Arms eased through seals
  Head eased through neck seal
  Set neck seal flat and check wrists
  Close zip, with assistance if required
  Squat to squeeze air out

## Slide 30: Preparation and dressing
Practical session covering previous sequence
  Preparing suit
  Inverting suit for entry
  Arms and head through seals
  Checking seals are flat
  Closing zip properly
  Expelling air from suit

## Slide 31: Correct weighting
Initially guess the weight and set up a weightbelt accordingly
Kit up in full diving equipment
Enter water with spare weights within reach, submerge vertically
Attempt buoyancy check:
  Breathe out
  Sink
  Breathe in
  Float up

## Slide 32: Correct weighting
  Adjust weight for neutral buoyancy – no air in suit
  Add weight to allow for buoyancy change due to later air consumption – about 2 kg
  Inflate suit slightly to regain neutral buoyancy
    Adds ‘comfort factor’
    Relieves ‘squeeze’
    Gives adequate insulation
    Minimises ‘air migration’
  On descent - add small amount of air to restore neutral buoyancy and comfort
  On ascent - vent air to maintain comfort factor and neutral buoyancy

## Slide 33: Correct weighting
Ankle weights may be used if feet float
If used:
  Consider weight as part of total
  Not as extra weight
When using an adjustable valve:
  Achieve neutral buoyancy as explained before
  Set valve so it starts to vent air
  No need to continually adjust during dive
  Press centre if over-ride is required
  During ascent manual venting may be necessary

## Slide 34: Buoyancy and Diving
  During dive
  Air in drysuit and BC will expand
  Controlled dumping of air equalises diver’s buoyancy
  Controls ascent
  Descent
  Buoyancy - check correct weighting
  Combined effect of diver’s body, drysuit and SCUBA - positive buoyancy
  May need additional weight
  Fine tuning with lungs
  Ascent

## Slide 35: Drysuit diving in safety
  Keep suit zipped up whenever in a boat
  Make sure controls not obstructed by other kit
  Do not dive overweighted
  Use BC for surface inflation and emergency buoyancy
  Ensure a thorough buddy check of ALL equipment
  Avoid overheating if zipped in a drysuit
  Use a drysuit for routine buoyancy
  Descend feet-first and add air to maintain buoyancy
  Ascend under control making sure to vent air from arms
  If ascent accelerates and vent cannot cope
    Pull neck seal or wrist seal

## Slide 36: Emergency actions
Blow-up / inversion:
  Usually caused by inflator valve sticking open
  Too much air in suit
  Failure to vent on ascent
Try to disconnect direct feed
If too blown up and unable to regain control:
  Flare arms out
  Flare fins to create drag
If head is down, air will migrate to feet:
  Beware of feet-first ascents
Diver should be able to restore head-up position by forward roll

## Slide 37: Emergency actions
Inversion at the surface
  Try forward roll into head-up position
  Continue to over-inflate suit until weight of legs causes toppling over
  Dump excess gas
  Inflate BC to regain horizontal
  Roll face-up by holding one arm out while pushing down hard with the other outstretched arm
  Buddy can assist with these actions

## Slide 38: Emergency actions
Flooded suit
  Rare but possible if zip or seals fail or suit torn
  Abort dive
  Use BC for buoyancy
  Weight of water in suit may make the exit difficult
After effects
  Loss of control following above could lead to:
    Striking surface obstructions
    Lung damage
    DCI
    Drowning,
    Shock
    Hypothermia
  Treat accordingly

## Slide 39: Emergency actions
Tight neck seals
  Sudden unconsciousness
    Tight neck seal
    Compression of neck seal on ‘carotid sinus’ in neck
  If it feels too tight, it IS too tight
    Carefully trim it to a more comfortable fit

## Slide 40: Drysuit diver rescue
  Bring the casualty to the surface using CBL
  Technique will vary depending on configuration of controls
  At surface inflate the casualty’s BC:
    To help maintain a suitable posture
    To provide support if AV is needed and neck seal is leaking

## Slide 41: Summary
Introduction: lesson objectives
Drysuit preparation and dressing
Correct weighting and buoyancy checks
Drysuit diving in safety
Emergency actions
  ‘Blow-up’
  Inversion
  Flooding
Drysuit diver rescue