## Slide 1
Search and Recovery
The Shot-line and its Uses

## Slide 2: Simple shot-line
Simple shot
  Advantages - it’s simple
  Disadvantages
    not easily made vertical
    does not adjust for tidal rise / fall
Keep line as short as practical

## Slide 3: Outline
Why use a shot-line?
Types of shot-line
Construction
Deployment / recovery

## Slide 4: What is a shot-line?
A datum point comprising:
Buoy
Line
Weight

## Slide 5: Shot-line usage
Why use a shot line?
  Marked entry / exit point - aids dive management and boat cover
  Shortest route to / from surface
  More comfortable/secure
  Datum point for searches
Why not use boat’s anchor?
  Not vertical - useful dive time is shortened
  Line moves with boat movement
  Cover boat should be mobile at all times

## Slide 6: Top tensioned shot-line
Adjusts for tidal rise and fall
Near vertical line for descent / ascent
Doesn’t remain vertical in a current
More complex
Top weight can become entangled
Counterweight

## Slide 7: Bottom tensioned shot-line
Similar to top tensioned
  Adjusts for tidal rise and fall
  Near vertical line for descent / ascent
  Doesn’t remain vertical in a current
  Can tangle
Aids shot recovery
May require work / effort at depth to set up

## Slide 8: Shot-line with waster
Keeps shot-line securely on wreck
Reduces risk of shot entanglement on recovery
Strength of ‘waster’ line critical
Requires work / effort at depth
Dive management

## Slide 9: Trail or ‘tide’ buoy
Tide
Tide

## Slide 10: Shot-line construction
Line
  Ease of handling: 15-20mm diameter
Length
  Depth plus a couple of metres
  Surplus line tidied at surface
Buoy
  50% more buoyancy than total hanging weight
Shot weight
  Adequate size to prevent dragging ~25kg
Counterweight
  5-10kg dependent on conditions

## Slide 11: Shot-line connections
Buoy, line, weights
  Karabiners
Attachments
  Karabiners
  Prusik knots
  Rolling hitch
Shortening line
  Karabiners
  Chain senneting
  Knotted sheepshank

## Slide 12: Shot-line deployment
Prepare before reaching the site
GPS / transits position fix
Deploy on command from cox’n
Tidal flow considerations
Once deployed, re-check

## Slide 13: Lifting the Shot
Controlled recovery
  Lift bag rating = weight of shot
  Fill bag
  Lift to surface from boat, by pulling on line
Buoyant recovery
  Lift bag rating > weight of shot
  Fill to send up, stay well clear
  Boat should stay clear of area
Recovery into boat
  Coil or ‘flake’ line
  Do not tip lift bag

## Slide 14: Summary
Why use a shot-line?
Types of shot-line
Construction
Deployment / recovery