## Slide 1
Underwater Photography
Introduction

## Slide 2: Underwater Photography
Course aims
Domestic arrangements
Locations
Timings

## Slide 3: Course outline
Basic Theory
  Optics
  Camera fundamentals
  Housings
  Camera functions
  Shooting techniques
  Photography underwater
Practical
Downloading
Review

## Slide 4
Underwater Photography
Optics

## Slide 5: Optics
Refraction
Distortion
Loss of light
Loss of colour
Loss of contrast

## Slide 6: Refraction physics
Bending of light when it travels from one substance to another
  Caused by different speed of light in different substances
  Amount of refraction depends on:
    angle of incidence
      bigger angle = more bending
      ‘normal’ incidence = no bending
    substance – eg, glass > water
    direction – eg air to water, water to air
      dense to less dense - away from normal
      less dense to dense - towards normal
    wavelength of light – red > violet
  Lenses and prisms

## Slide 7: Refraction and cameras
Light bends when medium changes
  Simplified camera
  No refraction effect on land
  Refraction effect underwater
Magnifying effect
Reduced coverage
  a = angle of coverage on land
  b = angle of coverage underwater
a
b
Film/sensor
Lens
Case

## Slide 8: Distortion
Light is bent more at the edges due to refraction
A dome port can reduce the effect
  Dome ports may require an extra lens
  Alternative is accept some distortion

## Slide 9: Loss of light
Absorption of light
  By the water
  By clouds and waves
Height of sun
  Midday sun gives maximum light
  Morning and evening sun gives minimum light

## Slide 10: Loss of colour
Effect of depth on colour
5m
10m
15m
20m
25m
30m

## Slide 11: Loss of contrast
Higher density of water and particles give a similar effect to that of fog on land

## Slide 12: Summary
Refraction
Distortion
Loss of light
Loss of colour
Loss of contrast

## Slide 13
Underwater Photography
Camera Fundamentals

## Slide 14: Camera fundamentals
Parts of a camera
Sensor
Resolution
Memory
File types
Exposure
Compacts and housings

## Slide 15: Parts of a camera
Lens assembly
  Lens – focus / zoom
  Aperture
  Shutter
Sensor
Processor
Memory
Batteries
Controls
Viewfinder / display
Flash

## Slide 16: Sensor
CCD or CMOS chip
Image made up of dots called pixels

## Slide 17: Resolution
Millions of pixels in one image
Typically 3000 x 2000 = 6MP
Quality described as dpi - dots (pixels) per inch
At 300dpi could print 10 by 6.66 inches

## Slide 18: Memory
Memory cards come in various physical sizes and capacities
Typically 512MB - 8GB

## Slide 19: File types
Card size | jpeg images | RAW images
256MB | 56 | 14
512MB | 113 | 28
1GB | 222 | 55
2GB | 444 | 111
4GB | 888 | 222
RAW = uncompressed
jpeg = compressed

## Slide 20: Exposure
Aperture
  Lets light into camera - variable
  f22 small f2.8 big hole
Shutter
  Opens to let light through aperture
  Shutter speed – 1/15th, 1/250th.......
Exposure
  Amount of light allowed in = shutter speed and aperture
  Big hole short time = small hole long time
Sensitivity
Low
High
f22
f16
f11
f8
f5.6
f4
f2.8

## Slide 21: Compacts and housings
Compacts
  Inexpensive
  Many features
  Shutter lag
  Limitations underwater
Housings
  Predominantly made from inexpensive polycarbonate
  Specific to camera
  Supplementary lenses and strobes needed for optimum performance

## Slide 22: Summary
Parts of a camera
Sensor
Resolution
Memory
File types
Exposure
Compacts and housings

## Slide 23
Underwater Photography
Housings

## Slide 24: Housings
Pre-dive checks
Post-dive checks
Maintenance
Dry practical

## Slide 25: Pre-dive checks
  O Ring
  Port
  Controls alignment
  Lanyard
  Power
  Settings
  Take a test exposure

## Slide 26: Post-dive checks
Still water tight
Power down
Soak in fresh water
Dry
Remove camera
Check O ring condition

## Slide 27: Maintenance
Cleaning O ring
  Remove using blunt instrument or credit card
  Wipe clean
  Lightly grease with silicone
  Replace
  Check for sand, hair etc

## Slide 28: Summary
Pre-dive checks
Post-dive checks
Maintenance
Dry practical

## Slide 29
Underwater Photography
Camera Functions

## Slide 30: Camera functions
Shooting modes
Exposure modes
Light meter
Exposure compensation

## Slide 31: Shooting modes
Auto
Program auto-assist
Movie / video

## Slide 32: Exposure
All these combinations give the same exposure
  increase aperture: decrease shutter speed
  vice versa
Correct exposure
f4
1/250
f5.6
1/125
f11
1/30
f16
1/15
f8
1/60
Aperture
Shutter speed
under-exposed
over-exposed
just right

## Slide 33: Exposure modes
Macro / close-up
Party / night
Portrait
Landscape
Sports
Stitch
Aperture priority
Shutter priority
Manual

## Slide 34: Light meter
Some more advanced cameras have a light meter for use in manual mode
Bars towards + overexposed
Bar in centre correct exposure
Bars towards - underexposed
+………0………-
+………0IIIIIII…-
+…IIIIIII0………-

## Slide 35: Exposure compensation
You may prefer more or less exposure than your camera suggests
+2 image will be two stops lighter
+1 image will be one stop lighter
f4
1/60
f5.6
1/60
-2 image will be two stops darker
f16
1/60
-1 image will be one stop darker
f11
1/60
0
f4
1/250
0
f5.6
1/125
0
f16
1/15
0
f11
1/30
0
f8
1/60
EV change
Aperture
Shutter speed

## Slide 36: Summary
Shooting modes
Exposure modes
Light meter
Exposure compensation

## Slide 37
Underwater Photography
Shooting Techniques

## Slide 38: Shooting techniques
Camera to subject distance
Natural light
Artificial light
Balanced light
Freezing the action
Depth of field
White balance
Filters
Composition

## Slide 39: Camera to subject distance
Aim to get as close as you can
Minimise the amount of water between the lens and subject
Don’t use zoom

## Slide 40: Natural light
In shallow waters use natural light
At depth for ‘monochromatic’ subjects

## Slide 41: Artificial light
Can either be from a strobe
Or a diver’s torch

## Slide 42: Balanced light
Exposure for the natural light and artificial lights are identical

## Slide 43: Freezing the action
Use a fast shutter speed, above 1/125s to keep the subject sharp

## Slide 44: Depth of field
Small aperture (eg f11) or landscape mode increases range of subjects in focus
Large aperture (eg f2.8) or portrait mode decreases range of subjects in focus

## Slide 45: White balance
Manually set the camera for the correct white balance for that particular depth - use a white or grey card.
Palm of hand also can work

## Slide 46: Filters
Filters can correct for the lack of red light - use in conjunction with manual white balance

## Slide 47: Composition
Use the rule of thirds and position the focal point of your image at one of the points
Picture should read from left to right

## Slide 48: Composition – left to right
Picture should read from left to right
8
4
8
4

## Slide 49: Summary
Camera to subject distance
Natural light
Artificial light
Balanced light
Freezing the action
Depth of field
White balance
Filters
Composition

## Slide 50
Underwater Photography
Photography Underwater

## Slide 51: Photography Underwater
Safety and skills
Shooting tips
Code of Conduct

## Slide 52: Safety and skills
Normal safety rules apply PLUS
  Task fixation
  Awareness
  Buddy diving
Skills
  Buoyancy and trim
  Task loading

## Slide 53: Shooting tips – dive planning
Obstructed lens
Patience
Approach down-current
Get close
Dive in middle of day
Stay shallow

## Slide 54: Shooting tips – Composition
Shoot up not down
Use bubbles
Frame the subject
Interesting shape, shine, shadow, silhouette, surroundings

## Slide 55: Shooting tips – Composition
Interesting shape
Look for colour contrasts

## Slide 56: Shooting tips – Composition
Shoot up not down
Isolate subject from background

## Slide 57: Shooting tips – Technical
Read the manual
Use slower shutter speeds
Bracketing
Wide angle and macro
Retouching software

## Slide 58: Code of Conduct
Code of Conduct
  produced by MCS
  supported by all diving agencies
Contents summary
  No novices
  No danglies
  Good buoyancy
  Take the easy options
  Choose willing subjects
  Thou shalt not kill

## Slide 59: Code of Conduct
Code of Conduct
  produced by MCS
  supported by all diving agencies
Contents summary cont’d
  Don't be greedy
  Don't stress
  Night dives - dip don't dazzle
  Don't leave trapped bubbles
  Watch where you're going
  Report pollution and damage

## Slide 60: Summary
Safety and skills
Shooting tips
Code of Conduct

## Slide 61
Underwater Photography
Practical

## Slide 62: Practical
Underwater
Logistics
First session
Review
Second session
Review

## Slide 63
Underwater Photography
Downloading

## Slide 64: Post-processing introduction
Golden Rule
Back-up your images!
Duplicate
Work on copied images

## Slide 65: Levels
Correct for the desired exposure

## Slide 66: Contrast
Boost contrast to make image stand out
Use ‘S’ curves if available

## Slide 67: Saturation
Add up to 10% to make the colours more vibrant

## Slide 68: Sharpening
Use unsharp mask to sharpen
Experiment with values
Don’t over sharpen

## Slide 69: Image storage
Rename the file to something meaningful
  baskingshark100507.jpg
  CHood_anglerfish1_Cornwall.jpg
Keyword and use image library software
Back it up!

## Slide 70
Underwater Photography
Summary

## Slide 71: Review
Practical lessons learnt
Open forum
Advanced underwater photography courses
Buoyancy & trim workshop
All images © Charles Hood